## Slide 1: MIPS Simulator
CS 3339 - Group 7
Members: Samantha Hanna, Vanny Bundick, Amul Poudel, John Parsons
Notes: Today we’ll be presenting our MIPS Simulator project. This project focuses on simulating how a MIPS processor executes instructions step by step, helping us better understand computer architecture.

## Slide 2: What is MIPS?
CS 3339 - Group 7
Diagram: https://medium.com/@csoham358/a-beginners-guide-to-risc-and-cisc-architectures-fc9af424db3b
Notes: MIPS is a RISC, otherwise known as a reduced instruction set computer,architecture, which means it uses a small set of simple instructions. This makes it easier to understand how a CPU works internally by using a simple fast and efficient instruction set. Diagram: https://medium.com/@csoham358/a-beginners-guide-to-risc-and-cisc-architectures-fc9af424db3b

## Slide 3: Project Overview
CS 3339 - Group 7
Simulates MIP instruction execution
Model CPU components
Show step-by-step processing
[Input Instructions] → [Simulator] → [Registers + Memory Output]
Notes: Our simulator takes MIPS instructions as input and processes them through simulated CPU components, producing outputs like register values and memory updates.

## Slide 4: INSTRUCTION MEMORY CONTROL DECODER ALU PIPELINE REGISTER FILE STAGES DATA MEMORY OUTPUT System Components
CS 3339 - Group 7
Some examples of how our system would work:
(ADD $t3, $t0, $t1)
PC → Instruction Memory
↓
Decode (ADD)
↓
Register File → Read $t0=10, $t1=5
↓
ALU → 10 + 5 = 15
↓
Register File → Write $t3 = 15
(SW $t3, 0($zero))
PC → Instruction Memory
↓
Decode (SW)
↓
Register File → Read $t3=15, $zero=0
↓
ALU → Address = 0 + 0 = 0
↓
Data Memory → Store 15 at address 0
Notes: These are the core components we simulated. Each one plays a role in executing instructions, similar to a real CPU. Internally, our simulator follows this pipeline for each instruction, ensuring accurate execution.“Our simulator models a full 5-stage MIPS pipeline, including IF, ID, EX, MEM, and WB stages. Each stage communicates through pipeline registers such as IF/ID and ID/EX, allowing multiple instructions to be processed simultaneously.
We also implemented control signals and a debug mode that shows the state of the pipeline at each cycle.
For simplicity, we assume no data or control hazards, so we do not implement forwarding or pipeline flushing.”

## Slide 5: Instruction Cycle Decode Execute Fetch Memory Write Back
CS 3339 - Group 7
PC → Instruction Memory → Reg PC → Instruction Memory → Register File → ALU → Data Memory → Register File
stage_IF() (Pipeline.py): fetches instruction list at PC and advances PC
IF_ID_Latch (Stages.py): holds fetched instruction and PC until next cycle
Instruction.py: provides Instruction objects and NOP used when the pipeline is empty
stage_ID() (Pipeline.py): reads register values
generate(opcode) (Control.py): defines the behavior of an instruct
RegisterFile.py: reads rs and rt vals
IF_EX_Latch (Stages.py): forwards register values
Decoder.py: extracts opcode, register numbers, imms, and targets from asm file
stage_EX() (Pipeline.py): selects operands, invokes ALU
ALU.py: performs logical operations
IF_MEM_Latch (Stages.py): forwards ALU result, reg_rt (for SW use), and zero flag
stage_MEM() (Pipeline.py): directs read, write, and PC operations
Memory.py: models data memory of MIPS
IF_WB_Latch (Stages.py): forwards ALU result and loaded memory values
stage_WB() (Pipeline.py): selects write destination then commits to the register file
RegisterFile.py: receives written values
Notes: Every instruction goes through this cycle. Our simulator models each of these stages step by step.

## Slide 6: Instruction Formats R-Type I-Type J-Type
Opcode | rs | rt | rd | shamt | funct
Opcode | rs | rt | immediate
Opcode | address
CS 3339 - Group 7
Execution Example:
add $t0, $t1, $t2 -> $t1 ----\ → ALU (add) → $t0
$t2 ----/
Notes: MIPS instructions come in three formats. Our simulator parses each format differently depending on the instruction type.This example shows how two register values are added in the ALU, and the result is stored in another register.

## Slide 7: Demo Time!
Simulator Workflow:
Read instruction
Parse instruction
Execute operation
Update registers/memory
CS 3339 - Group 7
To execute program:
Terminal -
python main.py asm file(or path to asm file)
Notes: Internally, our simulator follows this pipeline for each instruction, ensuring accurate execution.“Our simulator models a full 5-stage MIPS pipeline, including IF, ID, EX, MEM, and WB stages. Each stage communicates through pipeline registers such as IF/ID and ID/EX, allowing multiple instructions to be processed simultaneously.
We also implemented control signals and a debug mode that shows the state of the pipeline at each cycle.
For simplicity, we assume no data or control hazards, so we do not implement forwarding or pipeline flushing.”

## Slide 8: Expected Results
-----Final Register State-----
$zero($00): 0 $at ($01): 0 $v0 ($02): 0 $v1 ($03): 0
$a0 ($04): 0 $a1 ($05): 0 $a2 ($06): 0 $a3 ($07): 0
$t0 ($08): 10 $t1 ($09): 5 $t2 ($10): 5 $t3 ($11): 15
$t4 ($12): 5 $t5 ($13): 50 $t6 ($14): 0 $t7 ($15): 15
$s0 ($16): 20 $s1 ($17): 5 $s2 ($18): 15 $s3 ($19): 0
$s4 ($20): 0 $s5 ($21): 0 $s6 ($22): 0 $s7 ($23): 0
$t8 ($24): 0 $t9 ($25): 0 $k0 ($26): 0 $k1 ($27): 0
$gp ($28): 0 $sp ($29): 0 $fp ($30): 0 $ra ($31): 0
-----Final Memory State-----
00000000: 15
CS 3339 - Group 7
Notes: Our simulator successfully executes instructions and updates registers and memory correctly.

## Slide 9: What can we improve on?
CS 3339 - Group 7
Notes: Some thing we discussed we could improve on was creating a better graphical interface for the MIPS simulator. I didn’t really come up with a fancyway to output our final register states in decimal and our final memory state, and to improve I would probably spend a lot more time trying to create a more visually appealing GUI. Another improvement that the assignment mentioned was error handling. Our current program doesnt really handle any kind of exception handling, so if I wanted this program to be even more extensive I would spend more time recognizing possible hazards and how to implement handling for them such as forwarding or pipeline flushing.

## Slide 10: Q&A
CS 3339 - Group 7
Notes: Possible questions: how to improve it? - There are several ways we can expand this project, especially by adding pipelining and a graphical interface. We could also add error handling to protect against common errors seen in mips simulators - last slide.
What is forwarding/pipeline flushing: Forwarding and pipeline flushing are techniques used in computer processor design to manage hazards in a pipelined architecture, ensuring correct execution while maintaining high performance. Forwarding resolves data dependencies by bypassing the register file, whereas flushing clears incorrect instructions from the pipeline following a branch misprediction
If someone asks about BEQ and J instruction: The BEQ instruction conditionally changes the program counter based on a comparison. In our case, since the values are equal, the branch is taken and execution jumps directly to the label "skip".
This means the J instruction is completely bypassed. If the branch had not been taken, execution would continue sequentially and eventually hit the J instruction, which would then unconditionally jump to "end".
This demonstrates how conditional and unconditional jumps interact in control flow.

## Slide 11: Thank you!